## Slide 1: Arion v0.2 (9/30 release)
Futurewei Cloud Lab
10/7/2022

## Slide 2: Key deliveries
Sharding across multiple Arion Wings
CP version control based reconciliation
DP notification (direct path)
DP application based performance testing
E2E deployment tool with sanity check - complete guide and workflow

## Slide 3
Arion CP with sharding
XDP
Arion Agent
Arion Master
User Space
Kernel Space
Arion Wing 1
Cloud
control plane
Gateway goalstate
Agent / Node
Regional server/service
User inputs
XDP
Arion Agent
User Space
Kernel Space
Arion Wing N
CN/VPC controller
(Alcor NCM)
CN1
Vxlan partitioned traffic
Vxlan partitioned traffic
Vpc goalstate (with GW)
Partitioned gateway
routing
Partitioned gateway
routing
Partitioning and sharding
Data partitioning – Arion Master will partition the goal states per gateway group
Traffic sharding - Alcor supports consistent and well sharding (based on VNI and dest subnet) for CNs to balance/route the live traffic to selected gateway group
Shard key – VNI + dest subnet
  Source could be random
  Dest IP could be too distributed, thus causes too many ovs rules for CN
CN2
Allocate a vm from a vpc

## Slide 4
Arion Wing
Arion Agent
eBPF map
Sqlite
Worker
1
Grpc receiver thread
Arion master
1
DB background
worker
Neighbor updates with revisions
thread worker
sqlite neighbor table (table 1)
sqlite eBPF programming status table (table 2)
Thread pool task queue
Worker
n
eBPF programming with return code
Limitation:
Requires state to be idempotent (this version doesn’t require the result of previous versions)
Doesn’t solve the last mile of eBpf/ovs dump rules and auto healing (when someone deletes rule from it), relies on sync return code (eBpf) or async message (i.e. ovs barrier reply)
Dependency chain is do-able but requires refining of the current design, like exec_queue/poll
Current design:
Arion Master to allocate unique resource key
  Supports multi-level versioning (GW group/partition, VPC level, or even per resource)
  Supports strict order (lower qps) and relaxed order (higher qps)
Agent supports concurrency and eventual consistency
  competition scope is per resource key (90+% cases highly concurrent)
  same resource’s simultaneous updates will proceed in a newer version win fashion, with both succeed/rollback in a txn
    both succeed
    failed and rolled-back
6
8
sync-ed job:
txn {
syncly check and store key with revision in memory-cache
syncly invoke eBPF syscall with return code
}
triggers an async write to table1
If #3 returns successful, trigger an async write to table2
2
3 & 4
4
2
Concurrent HashMap
1
1
6
Reconciliation #1 - Arion Master and Arion Agent

## Slide 5
Resource Id (key) | Neighbor Info | Version
VNI + vpc_ip | Host IP, Host Mac, … | 1 / (and then) 6
Version (key)
1
2
3
4
6
Neighbor rule table (table1)
Programming journal
(table2)
Table 1 – Neighbor rule table
  neighbor table stores received (but may not be programmed later) per neighbor (means per key) and version
  serving best effort local on-demand lookup
  relies on local agent to provide eventual consistency with server
Table 2 – eBPF version programming journal table
  eBpf table (for real programming status) maintains versions of
    successfully programmed
    intended ignored (means earlier versions that doesn’t need to catch up)
    only for eBPF failed case, do not log to table2 and that is a gap version that we would like to catch
  for reconcile, to know from which version it failed to program eBpf
When neighbor received, for neighbor rule table
  Add or update neighbor
  Purge neighbor
When eBpf programming
  succeeds, then insert this version to table2
  intended ignored (treated as succeeded), insert this version to table2
  failed, then do not log to table2
When Agent started
  Select min(gap) between continuous version blocks from table2
Reconciliation #2 – Arion Agent local DB schema

## Slide 6
Arion CP Performance – User update neighbors to server, till gateway programming E2E latency
E2E latency here = server processing + server DB writing + server to agent transmitting + agent programming done
Test overall latency after grpc warmed up (push x = 10% * count warm-up states, but enforces 0 < x < 2000)
Start time – when the 1st neighbor insert/update (to server aka. ArionMaster) is called by user
End time – when the Nth neighbor (last in this update) is programmed in Arion Wing ebpf, means all neighbors are programmed on gateway node
Bottleneck is in server DB writing, which could be further improved
This result is before reconciliation (there’s some overhead in versioning control), after reconciliation there is 2-3% degradation
Load (states per update) | Overall Latency
5 neighbors | 0.9 ms
100 | 15 ms
1k | 60 ms
10k | 748 ms
100k | 3.8 s
1million | 39 s
Notes: NCM -> ACA 1 million latency is more than 20 seconds or more
With all 3 improvements (db schema, transmitting and local programming) it got improved by 70% and beyond

## Slide 7
eBPF Maps
Arion XDP
Arion Agent
User Space
Kernel Space
ArionWing
CN1
CN2
OAM receiver
OVS
Direct path
CN XDP
OAM info
Proposed in-band DP notification e2e
vm
vm
vm
vm
vm
vm
vm
vm
vm
GW DP (XDP)
GW
CN1
Direct path
CN2
OAM receiver
OVS
vm
vm
vm
vm
OAM packet via dedicated channel
Legacy out-of-band OAM notification (already implemented in Alcor CN)
vm
vm
vm
vm
After further study of CN and ArionWing behavior and issues we met, we propose the following DP notification e2e (adding an optional minor XDP component at CN side) for various reasons:
  Arion DP degradation (introduced by extra in-band OAM processing) is relatively small (<3% in terms of throughput difference)
  XDP/eBPF module at CN side is optional and data format is non-intrusive, the CN data path continues working with/without the module (of course it turns off DP notification capability with disabling CN XDP)
  Doesn’t need adjustment at ACA/OVS side
  Some working components in previous project were leveraged
Datapath notification (for direct path)
OAM sender
OAM packet via GW tunnel
Vxlan GW tunnel

## Slide 8
Datapath Redis performance benchmark
Redis benchmarking results show that redis commands with default parameters through Arion DP cluster are only about 4% slower in terms of request/s compared to direct. When running redis-benchmark with pipeline enabled and larger packet size, the throughput(request/s) between via Arion and direct is about the same for the redis benchmark test sets.
redis-benchmark -h {server_ip} -n 1000000;
  default parameters:
    1000000 requests
    50 parallel clients
    3 bytes payload
    keep alive: 1
redis-benchmark -h {server_ip} -d 1400 -P 50 -n 1000000 (use larger packet size and turn on pipeline for higher throughput)
  parameters:
    1000000 requests
    50 parallel clients
    50 pipeline requests
    1400 bytes in payload
    keep alive: 1

## Slide 9
E2E deployment tool with sanity check
New E2E modules created/involved:
Enhanced test/pseudo controller (in Alcor git repo) to be able to feed test data to each component and drive the sanity test
  Feed CN test data (GW routes)
  Feed gateway goal state
  Feed gateway deployment/setup data
DP controller
  to deploy Arion Wing cluster

## Slide 10: Roadmap
Phase 1.5 - End of September
Phase 2 – End of December
  Turn on on-demand lookup (solution by leveraging AF_XDP is designed, and ready to be implemented)
  Evaluate a stateful scenario for Arion GW
Git repo / module | Release
Arion DP | https://github.com/futurewei-cloud/arion-dp/releases/tag/v0.2.0
Arion Master | https://github.com/futurewei-cloud/arion-master/releases/tag/v0.2-alpha
Arion Agent | https://github.com/futurewei-cloud/arion-agent/releases/tag/v0.2-alpha
Alcor (E2E test controller) | https://github.com/futurewei-cloud/alcor/blob/master/docs/test/e2eTestWithArionSetup.adoc